## Slide 1
BTEC Level 3 · Applied Science · Unit 1 · Biology
BTEC Unit 1 Biology: Microscopy
Light and electron microscopes, magnification, resolution and measuring cells.
PowerPoint teaching resource
jdscience.co.uk
Microscopy
1 / 31

## Slide 2
Learning objectives
By the end of this lesson you should be able to:
1
Describe how a light microscope forms an image and name its main parts.
2
Distinguish magnification from resolution.
3
Calculate magnification, actual size and image size using the standard triangle.
4
Compare light and electron microscopes in terms of resolution, magnification and specimen preparation.
5
Choose an appropriate instrument for a stated observation.
jdscience.co.uk
Microscopy
2 / 31

## Slide 3
DO NOW
Prior knowledge
• Which knob do you use first when focusing a light microscope — coarse or fine?
• Why is a stain often used on a slide?
• If a cell is 25 µm long and the image is 25 mm long, what is the magnification?
• Which can see viruses more clearly — a school light microscope or an electron microscope?
Think first — answers are on the next slide.
jdscience.co.uk
Microscopy
3 / 31

## Slide 4
ANSWERS
Retrieval answers
• Coarse focus first with the lowest-power objective, then fine focus.
• To increase contrast so structures are visible.
• 25 mm = 25 000 µm. Magnification = 25 000 / 25 = ×1000.
• An electron microscope — viruses are usually below the resolution of a light microscope.
jdscience.co.uk
Microscopy
4 / 31

## Slide 5
The light microscope
Rays, lenses and contrast
jdscience.co.uk
Microscopy
5 / 31

## Slide 6
Light microscope schematic
• The lamp provides light that passes through the specimen.
• The objective lens produces a magnified real image.
• The eyepiece magnifies that image again.
• Total magnification = eyepiece × objective.
• The stage holds the slide; the coarse and fine wheels focus.
Original apparatus diagram for teaching labels.
jdscience.co.uk
Microscopy
6 / 31

## Slide 7
Using a light microscope safely and well
• Start with the lowest-power objective and the slide central on the stage.
• Move the objective close to the slide while watching from the side.
• Focus away from the slide using the coarse wheel, then refine with fine focus.
• Increase objective power only after the image is sharp.
• Use a coverslip to protect lenses and flatten the specimen. Wipe spills; never use the coarse wheel on high power.
jdscience.co.uk
Microscopy
7 / 31

## Slide 8
Magnification versus resolution
Magnification
• How many times larger the image is than the real object
• M = image size / actual size
• Can be increased with stronger lenses
• Empty magnification adds no new detail
Resolution
• The smallest distance between two points that can still be seen as separate
• Limited by the wavelength of the radiation used
• Light microscopes: about 0.2 µm
• Electron microscopes: about 0.1 nm (much smaller)
jdscience.co.uk
Microscopy
8 / 31

## Slide 9
The calculation triangle
• Write every quantity in the same unit before dividing.
• 1 mm = 1000 µm. 1 µm = 1000 nm.
• Actual size = image size / magnification.
• Image size = actual size × magnification.
• Show the substitution and the unit conversion — that is where marks are won.
jdscience.co.uk
Microscopy
9 / 31

## Slide 10
Worked example 1
• A mitochondrion image is 40 mm long. Magnification is ×20 000.
• Convert 40 mm to µm: 40 × 1000 = 40 000 µm.
• Actual size = 40 000 / 20 000 = 2 µm.
• Check: mitochondria are typically 1–10 µm, so 2 µm is sensible.
• If you forget to convert units, the answer will be wrong by a factor of 1000.
jdscience.co.uk
Microscopy
10 / 31

## Slide 11
Worked example 2
• A bacterium is 2.0 µm long. The drawing is 80 mm long.
• 80 mm = 80 000 µm.
• M = 80 000 / 2.0 = ×40 000.
• State the answer as ×40 000, not 40 000 alone.
• Include a scale bar on drawings in practical work.
jdscience.co.uk
Microscopy
11 / 31

## Slide 12
CHECK YOUR UNDERSTANDING
Magnification practice
• Image = 15 mm, M = ×400. Find actual size in µm.
• Actual = 8 µm, image = 4.0 cm. Find M.
• A scale bar labelled 5 µm measures 25 mm on the page. What is M?
Think first — answers are on the next slide.
jdscience.co.uk
Microscopy
12 / 31

## Slide 13
ANSWERS
Calculation answers
• 15 mm = 15 000 µm. Actual = 15 000 / 400 = 37.5 µm.
• 4.0 cm = 40 mm = 40 000 µm. M = 40 000 / 8 = ×5000.
• 25 mm = 25 000 µm. M = 25 000 / 5 = ×5000.
jdscience.co.uk
Microscopy
13 / 31

## Slide 14
Electron microscopy
Shorter wavelength, higher resolution
jdscience.co.uk
Microscopy
14 / 31

## Slide 15
Transmission and scanning
• TEM (transmission): electrons pass through a thin specimen; good internal detail.
• SEM (scanning): electrons scan the surface; good 3D surface appearance.
• Both require a vacuum, so living specimens cannot be viewed.
• Preparation can introduce artefacts — treat images critically.
• Colour in published electron micrographs is usually added afterwards.
jdscience.co.uk
Microscopy
15 / 31

## Slide 16
Choosing an instrument
Need to see…
Prefer
Why
Living pond microbes swimming
Light
No vacuum; colour; movement
Cristae inside a mitochondrion
TEM
High internal resolution
Surface of a pollen grain
SEM
Surface topography
Nucleus of an onion cell in class
Light
Large enough; simple prep
jdscience.co.uk
Microscopy
16 / 31

## Slide 17
STUDENT ACTIVITY
Unit conversions drill
8 minutes
• Convert 0.25 mm to µm and to nm.
• A drawing of a 30 µm cell is 12 cm wide. Calculate M.
• Write a two-sentence explanation of why increasing magnification alone may not reveal two close objects as separate.
jdscience.co.uk
Microscopy
17 / 31

## Slide 18
ANSWERS
Drill answers
• 0.25 mm = 250 µm = 250 000 nm.
• 12 cm = 120 mm = 120 000 µm. M = 120 000 / 30 = ×4000.
• Resolution, not magnification, limits whether two points appear separate. If they are closer than the resolution, they blur into one.
jdscience.co.uk
Microscopy
18 / 31

## Slide 19
Common misconceptions
Not quite
Higher magnification always means a clearer image.
Instead
Resolution decides useful detail.
Not quite
Electron microscopes are used in school practicals on living cells.
Instead
They need a vacuum; living cells are not used.
Not quite
µm and nm can be mixed in the same calculation without converting.
Instead
Convert to one unit first.
jdscience.co.uk
Microscopy
19 / 31

## Slide 20
Key terminology
Term
Meaning you should be able to write
Magnification
Image size ÷ actual size
Resolution
Smallest separable distance between two points
Objective
Lens nearest the specimen
Artefact
Structure created by preparation, not present in life
Graticule
Measuring scale in the eyepiece
jdscience.co.uk
Microscopy
20 / 31

## Slide 21
Teacher explanation — unit conversions
• Write a conversion line every time: 1 mm = 1000 µm = 1 000 000 nm.
• Convert the quantity that is not already in the unit you want.
• If both are converted, convert them to the same unit.
• A factor-of-1000 error is the most common calculation mistake in this topic.
• Estimate: a plant cell is tens of µm, a bacterium a few µm, a virus tens of nm.
jdscience.co.uk
Microscopy
21 / 31

## Slide 22
Eyepiece graticule — the idea
• The eyepiece graticule is a ruler you see superimposed on the specimen.
• Its divisions are not a fixed number of micrometres — they change with the objective.
• You calibrate it using a stage micrometer of known length.
• Then: actual size = number of eyepiece divisions × micrometres per division.
• Even if you cannot do the practical today, you should be able to describe the steps.
jdscience.co.uk
Microscopy
22 / 31

## Slide 23
Stains and contrast
Why stain
• Many cell parts are colourless in water
• Stain binds to some structures more than others
• Iodine stains starch; methylene blue stains nuclei
• Contrast makes measurement possible
Limits
• Staining often kills the specimen
• Too much stain hides detail
• Some structures still need EM to resolve
• Stain does not improve resolution
jdscience.co.uk
Microscopy
23 / 31

## Slide 24
CHECK YOUR UNDERSTANDING
Instrument choice
• Which microscope would you choose to watch living yeast budding, and why?
• Which would you choose to study the inner membrane of a mitochondrion?
• Why might a published SEM image of an insect eye look coloured?
Think first — answers are on the next slide.
jdscience.co.uk
Microscopy
24 / 31

## Slide 25
ANSWERS
Instrument-choice answers
• Light microscope — no vacuum, so living cells can be viewed.
• TEM — high internal resolution.
• False colour is often added after capture; electrons do not produce a natural colour image.
jdscience.co.uk
Microscopy
25 / 31

## Slide 26
Drawing rules for practical work
• Use a sharp pencil; no sketchy shading.
• Give a title and a calculated magnification or a scale bar.
• Label with ruled lines that touch the structure.
• Draw what you see, not what you remember from a textbook diagram.
• These habits are assessed in Unit 1-style practical write-ups.
jdscience.co.uk
Microscopy
26 / 31

## Slide 27
How to answer a 4-mark structure item
• In calculations, box the converted values before dividing.
• Write × before a magnification answer.
• If asked to compare microscopes, mention both magnification and resolution, plus living versus vacuum.
Mark-winning habit
• Name the particles.
• Name the forces.
• Link force to the property.
• Avoid 'it' without a noun.
jdscience.co.uk
Microscopy
27 / 31

## Slide 28
EXAM-STYLE PRACTICE
Exam-style practice
• Calculate the actual width of a cell if the image is 42 mm wide and the magnification is ×700. Give your answer in µm. (2)
• Compare the resolution of a light microscope with that of a TEM and explain the difference. (4)
• Give two reasons a scientist might still choose a light microscope rather than an electron microscope. (2)
Think first — answers are on the next slide.
jdscience.co.uk
Microscopy
28 / 31

## Slide 29
ANSWERS
Exam-style answers
• 42 mm = 42 000 µm. Actual = 42 000 / 700 = 60 µm.
• Light microscope resolution is about 0.2 µm; TEM is much smaller (about 0.1 nm). Electrons have a shorter wavelength than light, so two close points can be distinguished.
• Can view living specimens / cheaper / colour / easier sample preparation / portable. (Any two.)
jdscience.co.uk
Microscopy
29 / 31

## Slide 30
Plenary
• State the magnification formula.
• Define resolution in one sentence.
• Name one structure you would need an electron microscope to study clearly.
jdscience.co.uk
Microscopy
30 / 31

## Slide 31
Independent practice
• Complete the microscopy worksheet, including the calculation page.
• Practise unit conversions until they are automatic.
• Optional practical: calibrate an eyepiece graticule if your centre has the slides.
jdscience.co.uk
Microscopy
31 / 31